Home > Garage doors openers > Evolution > LM60EV

LM60EV

24 V DC gearmotor permanent lubrication

The state-of-the-art technology of the new Evolution line is the combination of a new logic and energy efficiency. Evolution garage door openers are equipped with the best radio performance ever – not only does it provide bi-directional radio – which means: the garage door opener does not only receive signals, but also sends signals back – above all it means that the receiver can handle both 433 MHz and 868 MHz frequency transmitters. TECHNICAL DATA Input voltage: 220–240 V, 50–60 Hz Motor: 24 V DC Max. pull force: 600 N Standby power: 0,8 W Noise level: 54 dB DRIVE Typ: 24 V DC gearmotor permanent lubrication Drive mechanism: Belt with two-piece trolley on steel rail Door height: adjustable up to 2,30-5,00 m Travel rate: 160 mm per second Lighting: LED turns on when the drive is activated; turns off 2.5 minutes after closing Door arm: adjustable, trolley unlocking device Receiver: 433 MHz + 868 MHz 6-band receiver Memory registers: 180 SAFETY Automatic stop: by pressing a button during forward or backward run and obstacle detection Force setting: automatic Overfl ow protection: Transformer overload protection and low voltage wiring for accessories Limit switch setting: electronic TÜV certified: TÜV-tested to meet EN12453. For doors up to 90 kg / 10,7 m² DIMENSIONS Length (overall): 8023CR5-3183 mm / 8025CR5-3372 mm / 8030CR5-3881 mm Rail length: 8023CR5-2998 mm / 8025CR5-3187 mm / 8030CR5-3696 mm Max. trolley movements of: 8023CR5-2520 mm / 8025CR5-2720 mm / 8030CR5-3225 mm Headroom required: 30 mm Hanging weight: 12 kg Max door height: 2,30-5,00 mm Max door weight: 90 kg Max door surface: 10,7 m² FURTHER FEATURES Convenient features: Soft-Start and soft-Stopp, automatic close		Accessories included / Two 2-channel remote control with 868 Mhz Rolling Code. Incl. battery typ CR2032 and key ring. / 75EV Illuminated Push Button / Manual Product catalog

C-Rail to 2,30-5,00 m door height	828EV Internet Gateway	772E Failsafe infrared sensor system	78EV Multifunction Wall Control